## Slide 1: Research Updates on GNN Species Discovery
Rui Xu
University of Southern California
May 6, 2026

## Slide 2
Research objectives
Objectives
Develop a graph network generation approach that allows GNN to self grow, evolve, and prune
Study network behavior during the GNN growth process
Study/Test systems
H/O system:
  H2-O2 oxidation: simplest reaction network for GNN development and tests
H/O/C system:
  CH4/C2H4/C2H6-O2 oxidation: small hydrocarbon reaction networks
  C4H6-O2 oxidation: less-resolved reaction network; relevant to modern solid fuel combustion
H/O/C/N system:
  Reactions are relevant to modern solid fuels and explosive chemistry, e.g., HTPB/AP combustion
  We can build the network following two general steps:
    Step 1: NH3-O2 reaction network
    Step 2: Hydrocarbon-N-O reaction network

## Slide 3
Current research task
Atom-based GNNs with species identifications
Use the existence of species inside given chemical kinetic models to train GNN
GNN evolves to self-grow and prune atomic nodes and bond edges
Two research directions are proposed:
  Direction 1: Minimum-unit growing GNN
  Direction 2: Multiple-node classification GNN
Will start with the H/O (H2-O2) system and a four-node, minimum-unit GNN configuration.

## Slide 4
Two research directions
Direction/Idea 1: Minimum-unit growing GNN
GNN grows in iterations by a minimum unit set of atom nodes (e.g., for H/O system, a minimum unit can be 2H + 2O atom nodes)
GNN is trained using the existence of species from literature kinetic model
…
Direction/Idea 2: Multiple-node classification GNN
GNN performs classification task to identify species
GNN is initiated with multiple atom nodes at O(10) size (e.g., for H/O system, about 50 H and 50 O atom nodes are initiated)
GNN is trained using using the existence of species from literature kinetic model
…
…
…

## Slide 5
Starting point – The four-node minimum unit
We started training a four-node minimum growing unit system as a starting point.
Define the minimum growing unit as 2 H atom nodes and 2 O atom nodes, and initialize them
Nodes with the same elements are permutationally invariant
GNN training follows a two-step procedure presented below
Embeddings (inputs)
H
O
H
O
Training data:
Existence of species in given chemical kinetic models
Species bond length vs. bond order data from chemistry database
Training outputs:
Node: existence probability in a species
Edge: bond order
: Atomic number
: Interatomic distances
Step 1
GNN message passing
Step 2
MLP training for outputs
MLP: Multilayer perceptron
(i.e., Neural network)

## Slide 6
GNN architecture breakdown
Embeddings (inputs)
H
O
H
O
: Atomic number
: Interatomic distances
H
O
H
O
Step 1: Message passing
H
O
H
O
Atom/Node (i.e., 1) receives messages () from its neighboring nodes (i.e., 2, 3, 4)
An aggregate vector, is calculated by taking the mean messages from its neighboring nodes
Example of Node 1 message passing

## Slide 7
GNN architecture breakdown
Step 2: MLP predictor for atom existence and bond orders
…
…
…
…
Node aggregates
from Step 1
64
Input
32
Hidden
1
Output
Node input:
Edge input:
Node Existence Predictor
Bond
Order
Predictor
193
64
…
32
1
Total loss function
where
BO: bond order of the i-j pair
p: probability of a node i within a species
for now, the weights of loss are 1 to 1 ratio:

## Slide 8
Training data
Types of the training data
Graphs with variations in interatomic distances generated randomly.
Existing species of H/O system are: H2, O2, H, O, OH, H2O, HO2, & H2O2.
The bond order information of the existing species will be estimated based on their inter-node distances (e.g., using Pauling bond order estimation).
H
O
H
O
H
O
H
O
H
O
H
O
Possible species: H2, O2
Possible species: OH, H, O
Possible species: H2O, O
H
O
H
O
H
O
H
O
Example training graphs
Possible species: H2O2
Possible species: HO2, H
Atom node
Possible bond edge (positive link)
Not a bond edge (negative link)

## Slide 9
Training loss example
y-log scale
Trained on 1000 H/O four-node data

## Slide 10
Training loss – Ten runs (robustness test)
y-log scale

## Slide 11
Test results – H2 + O2
Bond order value
Probability of a node/atom existing in a species
Edge thickness scales with the bond order
All the ten trained 4-node GNN models were tested on all the H/O species with variations on the interatomic distances.
The test species are: H2, O2, H, O, OH, H2O, HO2, & H2O2.
Model predictions on bond order and atom existence probability were tested against a variety of 4-node graph structures.
A satisfactory test on
one H2 molecule and one O2 molecule at their minimum-energy bond lengths
(i.e., H–H: 0.74 Å, O–O: 1.21 Å)

## Slide 12
Test results – H2 + O + O
H2 molecule with a stretched H–H bond, i.e., at 1.64 Å.
Weak bond order
Existence probability much lower than 1.0, meaning a possibility of radical formation
H2 molecule at its equilibrium structure

## Slide 13
Test results – O2 + H + H
O2 molecule with a stretched O–O bond, i.e., at 1.66 Å.
O2 molecule at its equilibrium structure

## Slide 14
Test results – H2O + O
Interesting observation: H atoms in water are barely interacting…
Stretched O–H bond: 1.76 Å.
H2O molecule with a stretched O–H bond
H2O molecule at its equilibrium structure

## Slide 15
Test results – HO2 + H
Stretched O–O bond: 1.66 Å.
HO2 radical at its equilibrium structure
HO2 radical with a stretched O–O bond

## Slide 16
Test results – H2O2
H2O2 at its equilibrium structure
H2O2 with a stretched O–O bond

## Slide 17
Test results – OH + OH and OH + O + H
Interesting observation:
Different existence probabilities in H and O may signal different reactivity.
Two OH radicals at their equilibrium structures
One OH radical at its equilibrium structures
A stretched O–H bond

## Slide 18
Test results – OH + OH and OH + O + H
Four radicals far apart from each other
Four radicals approaching to each other
Four radicals getting even closer

## Slide 19
Next steps – Direction 1: Minimum-unit evolution GNN
Evolution of the GNN
With the trained 4-node model, the GNN should process “knowledge” to infer a possible set of species from a given a four-node (2H+2O) configuration.
In the next iteration, a new set of minimum growing unit (2H + 2O nodes) will be added to the graph.
Ideally, the new GNN (i.e., with 4H + 4O nodes) does not need additional trainings, since the Iteration-1, 4-node GNN already has information about “all” species involved in the H/O system.
The GNN will evolve through iterations and converge when all the species are discovered.
H
O
H
O
H
O
H
O
Iteration 1
H
O
H
O
H
O
H
O
Iteration 2
Possible species: H2, O2
Possible species: H2, HO2, OH, O
Adding the minimum growing unit
…
Atom node
Possible bond edge (positive link)
Not a bond edge (negative link)
Undetermined edge

## Slide 20
Direction 2 – Multi-node classification GNN
Example: H/O system
Initially populate multiple nodes of H atoms and O atoms. For example, 50 H atoms and 50 O atoms.
Same training data, loss function, and training outputs as in Direction 1.
Atom node embeddings
Atomic number
Valence electrons
Electronegativity
Spin multiplicity
Bond edge embeddings
Interatomic distance
Embedding features (inputs)
O
H
O
H
O
H
O
H
O
H
O
H
O
H
O
H
Training data:
Existence of species in given chemical kinetic models
Species bond length vs. bond order data from chemistry database
Training outputs:
Node: existence probability in a species
Edge: bond order
Total loss function
where
BO: bond order of the jth pair
p: probability of a node i within a species
…
…
Note: The GNN is supposed to be fully connected. Not all the edges are displayed simply for visualization purpose.

## Slide 21
Direction 2 – More on training data
Types of the training data (same as in Direction 1 but with larger graph sizes)
Graphs with variations in inter-node distances (interatomic distances) generated randomly.
Existing species of H/O system can be obtained from chemical kinetic models, e.g., FFCM-2.
The bond order information of the existing species will be estimated based on their inter-node distances (e.g., using Pauling bond order formula).
O
H
O
H
O
H
O
H
O
H
O
H
O
H
O
H
…
Possible species:
O2, 2OH, H2O, HO2, H2, H, O, & etc.
O
H
O
H
O
H
O
H
O
H
O
H
O
H
O
H
Possible species:
H2O2, 2OH, H2, HO2, H, 2O, & etc.
O
H
O
H
O
H
O
H
O
H
O
H
O
H
O
H
Possible species:
2HO2, 2OH, 2H2, O2, & etc.
…
…
Atom node
Possible bond edge
(positive link)
Not a bond edge
(negative link)
Example training graph data
Note: The GNN is supposed to be fully connected. Not all the edges are displayed simply for visualization purpose.